13-26E Water is cooled by air in a cross-flow heat exchanger. The overall heat transfer coefficient is to be determined.

Assumptions 1 The thermal resistance of the inner tube is negligible since the tube material is highly conductive and its thickness is negligible. 2 Both the water and air flow are fully developed. 3 Properties of the water and air are constant.

Properties The properties water at 140(F are (Table A-9E)

The properties of air at 80(F are (Table A-18E)

Analysis The overall heat transfer coefficient can be determined from

The Reynolds number of water is

which is greater than 10,000. Therefore the flow of water is turbulent. Assuming the flow to be fully developed, the Nusselt number is determined from

and

The Reynolds number of air is

The flow of air is across the cylinder. The proper relation for Nusselt number in this case is

and

Then the overall heat transfer coefficient becomes

13-42 Water is heated in a double-pipe parallel-flow heat exchanger by geothermal water. The required length of tube is to be determined.

Assumptions 1 Steady operating conditions exist. 2 The heat exchanger is well-insulated so that heat loss to the surroundings is negligible and thus heat transfer from the hot fluid is equal to the heat transfer to the cold fluid. 3 Changes in the kinetic and potential energies of fluid streams are negligible. 4 There is no fouling. 5 Fluid properties are constant.

Properties The specific heats of water and geothermal fluid are given to be 4.18 and 4.31 kJ/kg.(C, respectively.

Analysis The rate of heat transfer in the heat exchanger is

Then the outlet temperature of the geothermal water is determined from

The logarithmic mean temperature difference is

and

The surface area of the heat exchanger is determined from

Then the length of the tube required becomes

13-81C The value of effectiveness increases slowly with a large values of NTU (usually larger than 3). Therefore, doubling the size of the heat exchanger will not save much energy in this case since the increase in the effectiveness will be very small.

13-84 Hot oil is to be cooled by water in a heat exchanger. The mass flow rates and the inlet temperatures are given. The rate of heat transfer and the outlet temperatures are to be determined. (

Assumptions 1 Steady operating conditions exist. 2 The heat exchanger is well-insulated so that heat loss to the surroundings is negligible and thus heat transfer from the hot fluid is equal to the heat transfer to the cold fluid. 3 Changes in the kinetic and potential energies of fluid streams are negligible. 4 The thickness of the tube is negligible since it is thin-walled. 5 The overall heat transfer coefficient is constant and uniform.

Properties The specific heats of the water and oil are given to be 4.18 and 2.2 kJ/kg.(C, respectively.

Analysis The heat capacity rates of the hot and cold fluids are

Therefore,

and

Then the maximum heat transfer rate becomes

The heat transfer surface area is

The NTU of this heat exchanger is

Then the effectiveness of this heat exchanger corresponding to C = 0.95 and NTU = 1.659 is determined from Fig. 13-26d to be

( = 0.61

Then the actual rate of heat transfer becomes

Finally, the outlet temperatures of the cold and hot fluid streams are determined to be

13-109 Cooling water is used to condense the steam in a power plant. The total length of the tubes required in the condenser is to be determined and a suitable HX type is to be proposed.

Assumptions 1 Steady operating conditions exist. 2 The heat exchanger is well-insulated so that heat loss to the surroundings is negligible and thus heat transfer from the hot fluid is equal to the heat transfer to the cold fluid. 3 Changes in the kinetic and potential energies of fluid streams are negligible. 4 The overall heat transfer coefficient is constant and uniform.

Properties The specific heat of the water is given to be 4.18 kJ/kg.(C. The heat of condensation of steam at 30(C is given to be 2430 kJ/kg.

Analysis The temperature differences between the steam and the water at the two ends of condenser are

and the logarithmic mean temperature difference is

The heat transfer surface area is

The total length of the tubes required in this condenser then becomes

A multi-pass shell-and-tube heat exchanger is suitable in this case.

# Text boxes

Water

140(F

8 ft/s

Air

80(F

12 ft/s

Water

25(C

Brine

140(C

60(C

Oil

160(C

0.2 kg/s

Water

18(C

0.1 kg/s

(12 tube passes)

26(C

Steam

30(C

18(C

Water

30(C